## Slide 1
0 deg Camber
-2.0 deg Camber
+2.0 deg shim 0.0 deg Camber
Desired Camber
As installed on A/C
Unable to use shim, bolt will not fit a 2 deg offset (hole center mismatch)
if strut holes enlarged or axle stub holes enlarged assy will move, NOT GOOD
Landing Gear Strut
Axle Stub (483-1)
Brake Torque Plate
2 deg Shim

## Slide 2
+2.0 deg Camber
Using shims of ¼ to ½ degrees maybe acceptable but 2 degrees is questionable
Landing Gear Strut
Axle Stub (483-1)
Brake Torque Plate
Washer .065”
0 deg Camber
Desired Camber
Bolt is mostly Shear and some Bending due to the axle is
flat against the strut face that takes up some of the bending loads
Touchdown load
Top Bolt is mostly in Bending due to the gap between the axle
flat and the strut face The bending loads are reacted by the area of the washer
not the entire axle flat. This moment has to be reacted by the bolt in bending.
This maybe all acceptable but for how long, fatigue cracking of the bolt may result.
If you do the math the washer would have to be about .065”
Touchdown load